## Slide 1: Lab08 Long Division
李品辰

## Slide 2: Outline
Pipeline
Generate
Long Division (Lab08)
  LongDiv.sv
  SPEC
  Hint
Grading Policy

## Slide 3: Outline
Pipeline
Generate
Long Division (Lab08)
  LongDiv.sv
  SPEC
  Hint
Grading Policy

## Slide 4: Pipeline

## Slide 5: Outline
Pipeline
Generate
Long Division (Lab08)
  LongDiv.sv
  SPEC
  Hint
Grading Policy

## Slide 6: Generate
在合成前就編譯完成，相較for迴圈較不易出錯
可以將assign、always block、submodule放在generate裡宣告
generate是將一份電路複製多份，for則是在編譯時unrolling
在nWave裡可以看到sub-block顯示，較好debug

## Slide 7: Outline
Pipeline
Generate
Long Division (Lab08)
  LongDiv.sv
  SPEC
  Hint
Grading Policy

## Slide 8: Long Division (Lab08)
LongDiv.sv
  長除法可以將龐大的除法器運算化簡為一連串的移位與減法操作

## Slide 9: Long Division (Lab08)
LongDiv.sv
  本次 Lab 將實作大數除法器 (in_num1[31:0] / in_num2[15:0])
  Cycle time 極短，無法直接使用 “/” 和 “%” 進行運算 (timing violation!)
  輸入為連續 (in_valid 持續為 1)
  輸出也必須為連續 (out_valid 持續為 1)
  “in_num2[15]” 必為 leading 1 (pipeline 級數固定)

## Slide 10: Long Division (Lab08)
LongDiv.sv
  Output should be reset after “rst_n”
  “out_valid” should be asserted within 100 cycles after “in_valid”.

## Slide 11: Long Division (Lab08)
SPEC
Input Signal | Bit Width | Definition
rst_n | 1 | Asynchronous active-low reset
clk | 1 | Global clock
in_valid | 1 | Set to 1 when the input is ready
in_num1 | 32 | Dividend
in_num2 | 16 | Divisor (in_num2[15] == 1’b1)
Output Signal | Bit Width | Definition
out_valid | 1 | Set to 1 when the output is ready
out_num1 | 17 | Quotient
out_num2 | 16 | Remainder

## Slide 12: Long Division (Lab08)
Hint
  使用 generate 語法來設計重複性值高的 pipeline 電路
  Pipeline 補充影片: https://www.youtube.com/watch?v=jOzW7kfr2p4