## Slide 1: Lab01 Combinational Circuit
張皓庭

## Slide 2: Combinational Circuit
The system takes four input numbers: in_num0 ~ in_num3
Perform the specified bitwise operations based on the block diagram:
  A = in_num0 XNOR in_num1
  B = in_num1 AND in_num3
  C = in_num0 XOR in_num2
  D = in_num2 OR in_num3
Then, group and calculate the sum
  E = max(A, B) + min(C, D)
  F = min(A, B) + max(C, D)
Convert E into its Gray code representation, the outputs are the Gray-coded E and F

## Slide 3: Combinational Circuit
Gray code representation:
  A Gray code has a property that the codes for successive decimal digits differ in exactly one bit
  Binary to Gray conversion:
  Gray to binary conversion:
Decimal | Binary | Gray
0 | 000 | 000
1 | 001 | 001
2 | 010 | 011
3 | 011 | 010
4 | 100 | 110
5 | 101 | 111
6 | 110 | 101
7 | 111 | 100

## Slide 4: Block Diagram

## Slide 5: Block Diagram (Example)
21
45
93
35
71
33
72
127
71
33
72
127
143
160
200

## Slide 6: Block Diagram (Example)
0010101
0101101
1011101
0100011
1000111
0100001
1001000
1111111
1000111
1001000
1111111
10001111
10100000
11001000
0100001

## Slide 7: Block Diagram

## Slide 8: Specification
Comb.sv
Input Signal | Bit Width | Definition
in_num0 | 7 | Random 7-bit unsigned numbers
in_num1 | 7 | 
in_num2 | 7 | 
in_num3 | 7 | 
Output Signal | Bit Width | Definition
out_num0 | 8 | The gray code of max(A, B) + min(C, D)
out_num1 | 8 | min(A, B) + max(C, D)

## Slide 9: Directory
tar -xvf ~es26dcsTA01/Lab01.tar
00_TESTBED
  TESTBED.sv
  PATTERN.sv
01_RTL
  01_run_vcs_rtl
  09_clean_up
  Comb.sv
02_SYN
  01_run_dc
  09_clean_up
03_GATE
  01_run_vcs_gate
  09_clean_up

## Slide 10: Command
cd Lab01/01_RTL/
vim Comb.sv (text editor)
  i (輸入模式)
  [Esc] (退回普通模式)
  :w (儲存)
  :q (結束)
gedit Comb.sv (text editor)
  view → Highlight Mode → Sources → Verilog
  If you use Windows/MacOS, you can use VSCode/Notepad++, or any editors you are used to using.

## Slide 11: RTL Simulation
cd Lab01/01_RTL/
./01_run_vcs_rtl (電路模擬)
./09_clean_up (清除波型檔)
./05_nWave (看波型)
  範例波型

## Slide 12: Synthesis
cd ../02_SYN/
./01_run_dc (電路合成)
./09_clean_up (清除合成結果)
  合成結果: (不能有Error、要有Area report、Timing report slack met、不能有Latch)

## Slide 13: Synthesis
合成的timing report中的slack必須≧0 (MET)
如果出現timing violation → Demo Fail ! (slack < 0)

## Slide 14: Synthesis
記得檢查是否合成出Latch和error
  可以在 syn.log 用 ctrl+F 尋找關鍵字Latch、error
如果出現 Latch、error → Demo Fail
可在 /02_SYN/ 中使用 ./08_check
  檢查 “latch”, “error”, “timing”, “area”

## Slide 15: Gate-Level Simulation
cd ../03_GATE/
./01_run_vcs_gate (電路模擬)
./09_clean_up (清除波型檔)
./05_nWave (看波型)
  範例波形

## Slide 16: Grading Policy
Pass the RTL & Synthesis & Gate-level simulation: 100%
  合成結果: (不能有Error、Timing report slack met、不能有Latch)
Demo2 打 6 折

## Slide 17: Upload
cd ../09_UPLOAD/
./01_upload (上傳 code)
./02_download [argument] (下載上傳結果)
  [argument] = demo1 or demo2
  檢查是否上傳成功 & 正確
Demo1: 2026/03/11 17:30:00
Demo2: 2026/03/11 23:59:59