## Slide 1
CA.sv Overall Architecture
CA Top
CA_Control
FSM + RAM Cmd
CA_DataPath
Multiple_Processor
Issue Decode + Tags
Mult_5Stage_Parallel
64-lane Dot Product
ACT_5Stage_Parallel
ReLU / RAT / CAT / BAT
PoT_5Stage_Parallel
Max Shift + Clamp
Matrix_Max
3Stage
x_mem
q_mem
k_mem
v_mem
score_mem
attention reuse
External
RAM
>
RAM cmd
v
issue / capture
^
ready / result status
<
rd_data
>
wr_data
out_valid / out_data
>
>
>
issue_mode + operands | mult_data + MT tag | activated 16-bit matrix
^
^
^
^
^
<
Q / K / V bypass ACT
blue=data
orange=control/status
purple=attention buffers
green=write/output
>

## Slide 2
CA.sv Data Flow
Main path: RAM read -> operand dispatch -> multiply -> activation -> PoT quantization -> writeback/output
External
RAM
Multiple_Processor
issue decode
Mult_5Stage_Parallel
64-lane dot product
ACT_5Stage_Parallel
activation
PoT_5Stage_Parallel
quantize to 4-bit
wr_data
External
RAM
out_data[31:0]
>
rd_data
>
matrix operands
>
NORM / FINAL path
>
activated 16-bit
>
packed 4-bit
>
<
last row token
v
Q / K / V bypass ACT
Attention Scratch Buffers
x_mem[0..3]
q_mem[0..3]
k_mem[0..3]
v_mem[0..3]
score_mem[0..7]
v
SHA / MHA capture
issue modes: IM_QKV / IM_SV / IM_FINAL
^
<
<
<
>
scratch feedback: Q/K/V, score, score*V
>
<
<
<
blue=data
purple=attention reuse
green=write/output