## Slide 1: DCS 2026 Spring Lab 3 - Sequential Circuit 2
TA : 陳孟頡 Advisor : Tian-Sheuan Chang
Date : 2026.03.19

## Slide 2: Lab03
Run the command below to get files for this lab.
  tar -xvf ~dcsTA01/Lab03.tar

## Slide 3: Sequential v.s. Combinational in Verilog
 | Sequential Circuit (D Flip-Flop) | Combinational Circuit
Verilog Code |  | 
Block Diagram |  | 
D
Q
reset
dff_next
clk
rst_n
dff
Adder
z=a+b
in1
in2
sum
a
b
z

## Slide 4: Example Counter
D
Q
reset
clk
rst_n
Adder
z=a+b
‘d1
a
b
z
count
count_next
Combinational
Sequential

## Slide 5: Example Counter
D
Q
reset
clk
rst_n
Adder
z=a+b
‘d1
a
b
z
count
count_next
0 (reset)
1
Cycle 0:

## Slide 6: Example Counter
D
Q
reset
clk
rst_n
Adder
z=a+b
‘d1
a
b
z
count
count_next
1
2
Cycle 1:

## Slide 7: Example Counter
D
Q
reset
clk
rst_n
Adder
z=a+b
‘d1
a
b
z
count
count_next
2
3
Cycle 2:

## Slide 8: Reminder
Reset all DFFs so you don’t start with unknown value.
Separate combinational and sequential part in your Verilog code.
Avoid multiple-driven net.

## Slide 9: Lab03: Sequential Sorting Network
Sorting Network:
  Sort N numbers using Compare-and-Swap units.
  Best for small N and ultra-low latency, parallel data.
in_data[0]
in_data[1]
in_data[2]
in_data[3]
in_data[4]
CMP
CMP
CMP
CMP
CMP
CMP
CMP
CMP
CMP
CMP

## Slide 10: Lab03: Sequential Sorting Network
Sorting Network:
  Sort N numbers using Compare-and-Swap units.
  Best for small N and ultra-low latency, parallel data.
in_data[0]
in_data[1]
in_data[2]
in_data[3]
in_data[4]
CMP
CMP
CMP
CMP
CMP
CMP
CMP
CMP
CMP
CMP
45
0
44
24
33
Ex:
45
44
33
24
0
45
0
44
24
33
45
0
44
24
33
45
0
44
24
33
45
0
44
24
33

## Slide 11: Lab03: Sequential Sorting Network
Input:
  5 unsigned 6-bit integer in serial.
Output:
  Consecutive 5 sorting results.

## Slide 12: SeqSort.sv
Input Signal | Bit Width | Definition
clk | 1 | Clock signal.
rst_n | 1 | Asynchronous active-low reset.
in_valid | 1 | High when in_data is valid.
in_data | 6 | Five Input data need to sort given in serial.
Output Signal | Bit Width | Definition
out_valid | 1 | Pull high when out_data is valid. Should be reset when rst_n is low.
out_data | 6 | The five sorting result in serial. Should be reset when rst_n is low.

## Slide 13: SeqSort.sv
Five input data provided in serial.
Five output sorting results (descending) in serial.

## Slide 14: SeqSort.sv
Outputs should be reset when rst_n is low.
out_valid should not overlap with in_valid.
out_valid should pull high in 100 cycles after in_valid pull low.
Five outputs must be consecutive.
out_data should be 0 when out_valid is low

## Slide 15: Grading Policy
1st demo – 100% for following requirements:
  Pass the RTL simulation
  Pass Synthesis (No Error, Timing Report Slack met, no Latch)
  Pass Gate-level simulation
2nd demo – 60%

## Slide 16: Upload
cd ../09_UPLOAD/
./01_upload (upload code)
./02_download [argument]
  [argument] = demo1 or demo2
Note:
  Make sure to upload the correct file successfully.
  Deadline:
    1st demo: 3/19 17:40
    2nd demo: 3/19 23:59
Good Luck !