## Slide 1: DCS 2026 Spring Lab 9 – CDC
TA : 陳孟頡 Advisor : Tian-Sheuan Chang
Date : 2026.05.14

## Slide 2: Lab09
Run the command below to get files for this lab.
  tar -xvf ~es26dcsTA01/Lab09.tar

## Slide 3: Clock Domain Crossing (CDC)
CDC: When the data launched and captured by different (asynchronous) clock domain, this case is called Clock Domain Crossing.
Consider two clocks, clk1 and clk2, with periods 13 and 10, respectively.

## Slide 4: Metastability
The unstable status due to non-ideal data transition is called metastability.
To avoid this phenomenon, we must ensure that data should be stable during setup/hold timing check.
However, CDC designs will inevitably face this problem.

## Slide 5: Solution: A Brute-Force Synchronizer
For more details, please reference to Lecture 12 - Metastability

## Slide 6: Convergence Issue
When transmitting multi-bit data, there is no guarantee that every bit will arrive at the same time
Reference: 2023 Fall iclab Lec07 (Jasper_CDC_introduction_lhlai)

## Slide 7: Solution 1: Handshake Synchronizer
Request-acknowledge protocol
High latency
Reference: 2023 Fall iclab Lec07 (Jasper_CDC_introduction_lhlai)

## Slide 8: Solution 2: FIFO Synchronizers (Asynchronous FIFO)
Read/Write data in different clock domain with a dual-port RAM.
Use gray-coded pointers to generate full and empty status flags.
High throughput with hardware overhead.
Reference: 2024 Fall iclab Lec07 (IC設計簡介 - Clock Domain Crossing(CDC))

## Slide 9: Asynchronous FIFO : Bit Number of Pointers
raddr[2:0] = 3'b000
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
Write Pointer
Read Pointer
waddr[2:0] = 3’b000
waddr[3:0]
raddr[3:0]

## Slide 10: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[2:0] = 3’b000
raddr[2:0] = 3'b000
Data 0

## Slide 11: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[2:0] = 3’b001
raddr[2:0] = 3'b000
Data 0
Data 1

## Slide 12: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[2:0] = 3’b010
raddr[2:0] = 3'b000
Data 0
Data 1

## Slide 13: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[2:0] = 3’b111
raddr[2:0] = 3'b000
Data 0
Data 1
Data 2
Data 3
Data 4
Data 5
Data 6
Data 7

## Slide 14: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[2:0] = 3’b000
raddr[2:0] = 3'b000
Data 0
Data 1
Data 2
Data 3
Data 4
Data 5
Data 6
Data 7
Empty? Full?

## Slide 15: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[3:0] = 4’b0000
raddr[3:0] = 4'b0000
Data 0

## Slide 16: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[3:0] = 4’b0001
raddr[3:0] = 4'b0000
Data 0

## Slide 17: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[3:0] = 4’b0111
raddr[3:0] = 4'b0000
Data 7
Data 0
Data 1
Data 2
Data 3
Data 4
Data 5
Data 6

## Slide 18: Asynchronous FIFO : Bit Number of Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[3:0] = 4’b1000
raddr[3:0] = 4'b0000
Data 7
Data 0
Data 1
Data 2
Data 3
Data 4
Data 5
Data 6
EMPTY
if (waddr == raddr)
FULL
if (waddr == {~raddr[3], raddr[2:0]})

## Slide 19: Asynchronous FIFO : Gray-Coded Pointers
Address | Data
7 | 
6 | 
5 | 
4 | 
3 | 
2 | 
1 | 
0 | 
Dual-port RAM
waddr[3:0] = 4’b0001
raddr[3:0] = 4'b0000
Data 0
Data 1
waddr[3:0] = 4’b0010
Convergence Issue

## Slide 20: Asynchronous FIFO : Gray-Coded Pointers
Single-Bit Flip: Only one bit changes between consecutive values.
Simple Logic: Easily converted from binary using a single XOR shift operation:
Decimal | Binary | Gray Code
0 | 000 | 000
1 | 001 | 001
2 | 010 | 011
3 | 011 | 010
4 | 100 | 110
5 | 101 | 111
6 | 110 | 101
7 | 111 | 100
For more details, please reference to Lecture 12 - Metastability
How to determine full condition if using gray-coded pointer instead of binary?

## Slide 21: Lab09 : Asynchronous FIFO
tx_clk = 2.5ns, rx_clk = 14.1ns
Write data into the FIFO in TX domain.
Read data from FIFO in RX domain.
Fill the blanks in AsyncFIFO.sv to complete the Asynchronous FIFO.

## Slide 22: Lab09 : Block diagram

## Slide 23: AsyncFIFO.sv
TX Domain Signals:
Signal | I/O | Bit Width | Definition
tx_clk | input | 1 | Write domain clock signal.
tx_rst_n | input | 1 | Write domain asynchronous active-low reset.
tx_valid | input | 1 | High when tx_data is valid.
tx_data | input | 8 | Data need to write into FIFO.
tx_full | output | 1 | High when FIFO is full.

## Slide 24: AsyncFIFO.sv
RX Domain Signals:
Signal | I/O | Bit Width | Definition
rx_clk | input | 1 | Read domain clock signal.
rx_rst_n | input | 1 | Read domain asynchronous active-low reset.
rx_valid | output | 1 | High when rx_data is valid.
rx_data | output | 8 | Data read from FIFO.
rx_ready | input | 1 | High when PATTERN.sv is ready to read data.

## Slide 25: Waveform
TX domain randomly send write data
RX domain randomly set ready signal
rx_valid should be high when rx_data is valid

## Slide 26: Waveform
tx_full should pull high when FIFO full

## Slide 27: Reminders
Using the TA's provided framework is strongly advised.
All needed signals are already defined, but feel free to add your own.

## Slide 28: Hint : TX Domain Architecture

## Slide 29: Hint : RX Domain Architecture

## Slide 30: Hint : Synchronization

## Slide 31: Hint : FIFO Full/Empty
TX domain full
  Compare tx gray-coded pointer to rx gray-coded sync pointer.
RX domain empty
  Compare rx gray-coded pointer to tx gray-coded sync pointer.
tx_full
rx_empty

## Slide 32: Grading Policy
1st demo – 100% for following requirements:
  Pass the RTL simulation
  Pass Synthesis (No Error, Timing Report Slack met, no Latch)
  Pass Gate-level simulation
2nd demo – 60%

## Slide 33: Upload
cd ../09_UPLOAD/
./01_upload (upload code)
./02_download [argument]
  [argument] = demo1 or demo2
Note:
  Make sure to upload the correct file successfully.
  Deadline:
    1st demo: 5/14 17:20
    2nd demo: 5/14 23:59